Att King Springs Distributors

TOYOTA LANDCRUISER 200 SERIES WITH

KDSS SYSTEM

Please note when fitting King Springs to Toyota Landcruiser 200 Series or Lexus LX Series vehicles fitted with Toyota’s Kinetic Dynamic Suspension System (KDSS),

also referred to by Toyota as a “hydro-mechanical semi active anti roll bar”

Please be advised of the fitting procedure:

1. Suspend vehicle on 2-post type chassis hoist allowing wheels to hang.

2. Locate the KDSS valve housing.

NOTE: The valve housing is located on the left-hand side of the

vehicle, on the inside of the chassis rail, roughly half way

between the front and the back of the vehicle.

3. Using a 5mm hex key, open the 2 leveling valves 3 full rotations anti-clockwise.

(Access is from underside of the KDSS valve)

NOTE: The KDSS system is now open and the sway bar ends

should be able to be freely manipulated with little effort,

allowing spring / strut removal and installation.

NOTE: THE VEHICLE MUST NOT BE DRIVEN WITH

THESE VALVES OPEN AS THIS WILL COMPRIMISE THE SYSTEM AND RENDER THE VEHICLE UNSAFE TO DRIVE.

4. With the vehicle sitting on level ground, close both KDSS leveling valves by turning them

in a clockwise direction and then tightening.